- AXMER Review

The following rules changes and definitions have been changed:

- proposed resting hours 8 h

## II. 18	DETAILS FOR TIME LIMITS (rest hours) (5.6)

The hours between <*xxxx and yyyy*> local time will be disregarded for the purpose of the time limits of complaints and protests. The total rest period per day shall be a minimum of 8 10 hours and may be divided into two parts, depending on the daylight period.

- Use of turning vents

3.1.3	The use of vents which are designed to rotate or propel a balloon is prohibited. Turning vents may only be operated in flight for the purpose of orienting the basket after all tasks are completed. Prolonged or excessive use of the turning vents is prohibited. Penalty 250 to 500 task points.

- Minimum distance to further/other goals

8.4.7	If not otherwise stated in the Task Data, the minimum distance from the launch point to a goal/target applies as well to all further other goals/targets set by the director on that flight.

- finetuned definition of ILA/ILP

## 9.2	INDIVIDUAL LAUNCH AREAS

9.2.1	Individual launch areas are selected by the competitors. The boundary of the launch area is a circle of 100 meter radius from the position of the basket at the start of hot inflation. the individual launch point or the physical boundary of the area if closer.

9.2.3	In tasks where competitors select an individual launch area, the INDIVIDUAL LAUNCH POINT (ILP) is the position of the basket at the start of hot inflation take-off.

- distance penalty at landings

13.3.4.	Competitors landing in an MMA will not achieve a result in the related task. If no MMA is set, landing within 200 meters of goals/targets or any physical mark of the competitor will be penalised up to 200 task points.

11.2.2	Unless otherwise stated in the task data, a landing at will is not permitted within a MMA where a target is displayed or if no MMA is set, within 200 meters of any goal/target set by the Director or selected by the competitor or any physical mark of the competitor (for penalty see distance infringements).

11.3.4	Unless otherwise stated in the task data, a contest landing is not permitted within 200 meters of goals/targets any goal/target set by the Director or selected by the competitor or within a MMA (for penalty see distance infringements).