HANDICAP LIST

For the 1st World Gliding Championships - Club Class, the following handicaps will be used. Gliders which fall in the range of 1.020 through to and including 0.940 are eligible to compete.

HANDICAP ADJUSTMENTS

Glider weights

Glider reference weights shown above are based on typical empty weights found within Australia plus 110Kg.

The glider handicap is based on the performance of that glider at a stated handicap weight. Gliders flown at lower weights (where this is a choice) will not have their handicaps adjusted.

Gliders may carry non-disposable ballast provided that the pilot/glider combination does not exceed the reference weight.

Pilots must nominate a flying weight which must remain constant for the whole competition. Pilots found to be varying from this weight will attract a penalty.

Where a glider is flown at a higher weight, by necessity (due to the weight of the glider and/or the pilot), the handicap will be increased by .002 for each 10kg or part thereof that the glider exceeds the base handicap weight.

Winglets (where not standard) will attract an additional handicap of .005.

Wing fillets (where these are substantial and non-standard) will attract an additional handicap of .002.

Wingspan There will be no additional handicap if the wingspan is 1 cm or less above the nominal wingspan of the standard glider. Where the wingspan  exceeds this, there will be an additional handicap of .001 per centimetre of excess wingspan. The wingspan will be measured as described in the Sporting Code.

Significant drag reduction measures involving noticeable changes to the shape of wings or fuselage will attract an additional handicap of .002 per measure. This does not apply to profile sealing of control surfaces, smoothing or sealing of canopy or surface gaps, or provision of sealing flaps over openings such as aerotow or winch releases.

# Text boxes

TYPE	H’CAP	WT

SALTO	1.04	306

IS29D	1.04	360

ASW 15	1.02	318

ASW 15B	1.02	360

ASTIR CS/77	1.02	380

COBRA	1.02	370

LIBELLE STD	1.02	320

CIRRUS STD	1.00	335

DG 100	1.00	357

HORNET	1.00	364

JANTAR STD 1	1.00	365

LIBELLE OPN	1.00	300

LS 1F	1.00	364

ASW 19 B	0.98	380

CIRRUS OPN	0.98	335

DIAMANT 16.5	0.98	390

JANTAR STD 2	0.97	385

JANTAR STD 3	0.97	390

PIK 20A	0.96	360

PIK20 B	0.96	364

PIK 20D	0.96	359

TYPE	    H’CAP	WT

DG 300		0.96	367

LS 4		0.95	380

LS 4A		0.95	381

LS 7		0.94	345

ASTIR speed	0.94	375

DG 200		0.94	360

DG202		0.94	360

MOSQUITO	0.94	379

MINI NIMBUS	0.94	366

PIK 20E		0.94	437

ASW 24		0.94	352

DG 400 (15)	0.94	427

DISCUS (a/b)	0.93	363

KESTREL(17)	0.93	390

LS 3		0.93	408

LS 3A		0.93	380

SZD 55		0.93	336

H304		0.93	355

H304cz		0.925	347

LS 8		0.92	350

ASW24E		0.90	415